## Slide 1: Water Neutral Growth in the Town of Ipswich Integrating Land Use Planning and Water Conservation Strategies to Build Climate Resiliency for the Future
PIE-Rivers Partnership Annual Meeting
December 5, 2019

## Slide 2: Town of Ipswich Water sources
Parker river watershed
  Browns, mile lane wells
  Dow & Bull brook reservoirs
Ipswich river watershed
  Essex road, fellows road & Winthrop WEll

## Slide 3
Source restrictions (Manganese, infrastructure age)
Regulatory (emerging contaminants) and Sustainable Water Management Initiative (SWMI)
Drought vulnerability (2016 Drought)
Land use changes/development pressures (more impervious surface, water quality impacts, increased water demand)
Climate change
…. have led to a Community discussion of water needs, climate impacts, and resiliency
Current challenges
Notes: Ipswich river sources capped at existing (safe yield) and parker river sources subject to SWMI - Basically there’s no more water available and summer use needs to go down

## Slide 4: What Happened in 2016?
Significantly Below average precipitation
High customer water demand
Reduced capacity Browns & Fellows Road Wells – manganese (MN)
Required emergency declaration by dep
Dry River bed (environmental and recreational impacts)
Community response
  Regulation updates
  Water restriction by-law
    including private wells
  Heightened concern about water
Bull Brook Reservoir
2016
Notes: Maybe not as much detail on this slide?

## Slide 5
Increasing concern over development impacts inside and outside of water supply protection zones
  expansion of impervious surfaces
    Water quality
    Recharge
    erosion
  Increased water demand
Land use & development

## Slide 6: Climate Change: Expected changes/impacts
  Extreme weather
    Power, equipment failures, facility damage
  More droughts/greater magnitude
    Strains ability to meet demand
    Threatens natural water cycle
  More frequent & heavy rainfall
    Flooding, Erosion
    Sediment accumulation
  Sea level rise
    Potential salt water intrusion

## Slide 7: Existing initiatives
Water supply protection
  By-Law
  2,000 acres surface & groundwater protection zones
Demand management
  Monthly billing
  Smart Meters
  Residential Seasonal Rate Structure
    15% drop in total annual water use
    24% drop in summer residential water use
  Drought Management Plan
  Water Restriction By-law
Education through Greenscapes North Shore Coalition

## Slide 8: Still need to Reduce vulnerability & build resiliency
Build redundancy, reliability, resiliency
  Infrastructure improvements
  Water Supply Protection
  Water Demand management
  Education & Outreach
Basis for MAPC Grant Project with Ipswich River Watershed Association
Water Neutral Growth Project Goal:
Reduce existing water use to the maximum extent possible, especially during periods of lower water availability, and minimize additional demand created by future growth and development
Notes: Maybe not as much detail on this slide?

## Slide 9: Water neutral growth grant project Recommendations: minimization & offsets
Land Use: water use minimization through water neutral growth bylaws, low impact development & stormwater regulations, and incentives
Water Bank/In Lieu Fee programs: recommendations for water use mitigation programs (aka “WUMP”)
enhanced water Conservation Strategies: completing a water Use Profile analysis to drive recommendations & strategies
Notes: What we’ve done over the year

## Slide 10: Land Use Recommendations
Establish a clear permit review process that considers water use for all new and redevelopment projects
Review current bylaws using tools such as Mass Audubon’s Tool for Low Impact Development & Climate-Smart, Nature-Based Solutions
Adopt a Water Neutral Growth Bylaw that requires developments to achieve “net zero” water use through minimization and offsets
www.massaudubon.org/our-conservation-work/advocacy/shaping-the-future-of-your-community/saving-land-water-money-with-lid
Notes: 1. Town should establish permit review process to effectively implement adopted water savings recommendations for all new and re-development projects
2. Ipswich should adopt a Water Neutral Growth Ordinance that requires developments achieve net zero through minimization and offsetting their projected additional water demand. Incentive use of grey water and rainwater re-use as a central component.
3. Ipswich should undertake a thorough review of its development by-laws to minimize water use - bylaws (including for building permits exempt from planning/zoning review) should mandate maximum implementation of LID-related requirements and make OSRD the norm for subdivisions

## Slide 11: Stormwater Solutions
Treat rainwater as a resource not a waste product or problem
Using GIS, identify best sites for maximizing infiltration of stormwater through green infrastructure and/or a drought resilience zoning overlay district
Update stormwater bylaw to prohibit the discharge of stormwater runoff to the maximum extent feasible from every parcel (100% infiltration)
Meet the requirements of the epa ms4 permit
Notes: - Using GIS, identify best sites for maximizing infiltration of stormwater through green infrastructure and/or a drought resilience zoning overlay district
- Update stormwater bylaw to prohibit the discharge of stormwater runoff to the maximum extent feasible from every parcel (100% infiltration)
- Meet the requirements of the epa ms4 permit

## Slide 12: Water Use Mitigation Recommendations Water Bank – In Lieu Fee Programs
Water use mitigation mechanisms can reduce or eliminate the strain of new development on the community’s water system
Notes: Ipswich watershed neighbors Danvers and Wenham currently have water use mitigation programs. Describe recommended WUMP for Ipswich.

## Slide 13: Ipswich Draft “WUMP”
Back of the envelope calculations….
Residential Development Projects Approved by Planning Board* 2015 – 2019
* Need to capture development that does not go through Planning Board permitting
7 Projects, Totaling 80 Bedrooms
Estimated WUMP Revenue (residential): $80,000 over the 5 years
Funds to support additional conservation efforts
Water audits, rebates, retrofits, educational programming, etc.
Notes: Commercial not calculated, what are the complications –
Focus more on mitigation than fee collection
Describe residential calculations
$80,000 over 5 years – could fund enhanced water conservation programs
Explain commercial questions ….

## Slide 14: Enhanced Water Conservation Strategies
Analysis of the Town’s individualized water use patterns to inform customer-specific conservation strategies
Water Loss Control review - American Water Works Association (AWWA) M36 “Top-Down” Audit
Adoption of recommendations from the recently completed Massachusetts Water Conservation Standards (July 2018)
www.mass.gov/massachusetts-water-conservation-standards
Notes: Highlights of the analysis include:
- Single family residential uses about 60% of the water in town and use increases by about 25% in the summer. The top 10% of summer water users use ~30% of summer residential water.
Commercial users are the 2nd largest water use group and use about 20% of water in town and use increases by about 25% in summer. Most commercial users don’t increase water use in summer; the increase in water use is due to ~10% of the accounts.
Minimize real and apparent losses by meeting or demonstrating steady progress towards an unaccounted-for-water (UAW) percentage of 10% or less
Enhanced water conservation measures give examples including community-based social marketing toolkit

## Slide 15: Town of Ipswich Water Use Data Analysis MA Division of Ecological restoration – 11/20/19
Data disclaimers:
All data presented is an average of 2017 and 2018
Summer use is defined as May-September
Winter use is defined as November-March
Discretionary use is calculated by subtracting total winter use from total summer use

## Slide 16
Chart: Cumulative Percent of Single-Family Residential Discretionary Use by Customer Percentile

## Slide 17
Chart: Cumulative Percent of Commercial Accounts Total Summer Usage by Account Percentile

## Slide 18: Water Use Profile Analysis Drives Water Conservation Strategies
Results Point Town Focus Toward:
  Specific Commercial Customers
    Audits
    Education
  Regional Residential Customers
    Rebates
    Education – including MA DER/DEP Community-based Social marketing
Notes: Land use regulations and development patterns in the Ipswich Basin communities are impacting water availability. Recommendations aimed at “water-neutral growth” include: adoption of a new ordinance to require developments to offset their projected additional water demand; review of bylaws to find opportunities to require and/or incentivize low impact development practices and green infrastructure; and recommended conditions for water use minimization which are available to permitting boards and committees. All of these tools will enable the community to work towards water neutral growth.
Water use mitigation mechanisms can reduce or eliminate the strain of new development on the community’s water system. A few other Massachusetts towns (including Ipswich watershed neighbors Danvers and Wenham) currently have water use mitigation programs. This report summarizes the lessons learned by these communities and the benefits to Ipswich in adopting this tool, and sets forth a recommended WUMP for Ipswich.
While gains have been made toward reducing water use across the Ipswich watershed over recent decades, there is more that can be done, especially in the summer when water use is the highest, there is the least amount of water available, and the threat of drought is highest. An analysis of the Town’s individualized water use patterns developed a water use profile which can inform customer-specific conservation strategies. Enhanced water conservation practices for Ipswich include: adoption of recommendations from the recently completed 2018 Massachusetts Water Conservation Standards, community-based social marketing practices promulgated by the MA Department of Environmental Protection and the Division of Ecological Restoration, and other new technological tools.

## Slide 19: Water Conservation Strategies
Address summer irrigation: prohibit automatic sprinklers or require rain sensors; consider irrigation sub-metering and billing (higher fees for irrigation); education
Indoor water audits: rebates, assistance, leak repair (businesses as well as residential)
Outdoor water audits: educate about water-wise landscapes; rebates for removal of high-water-use plants and sod and replacement with less water-intensive vegetation
Seasonal limits & restrictions: on watering within 48 hours of measurable rainfall; washing of hard surfaces (sidewalks, patios, driveways, siding); personal car washing; operation of non-circulating fountains; filling of swimming pools
Municipal buildings: audit Town Hall and all town buildings and properties for indoor and outdoor water efficiencies, with educational signage
Business audits: opportunities to work with commercial users including agricultural and recreational related businesses whose summer use is high
Notes: Land use regulations and development patterns in the Ipswich Basin communities are impacting water availability. Recommendations aimed at “water-neutral growth” include: adoption of a new ordinance to require developments to offset their projected additional water demand; review of bylaws to find opportunities to require and/or incentivize low impact development practices and green infrastructure; and recommended conditions for water use minimization which are available to permitting boards and committees. All of these tools will enable the community to work towards water neutral growth.
Water use mitigation mechanisms can reduce or eliminate the strain of new development on the community’s water system. A few other Massachusetts towns (including Ipswich watershed neighbors Danvers and Wenham) currently have water use mitigation programs. This report summarizes the lessons learned by these communities and the benefits to Ipswich in adopting this tool, and sets forth a recommended WUMP for Ipswich.
While gains have been made toward reducing water use across the Ipswich watershed over recent decades, there is more that can be done, especially in the summer when water use is the highest, there is the least amount of water available, and the threat of drought is highest. An analysis of the Town’s individualized water use patterns developed a water use profile which can inform customer-specific conservation strategies. Enhanced water conservation practices for Ipswich include: adoption of recommendations from the recently completed 2018 Massachusetts Water Conservation Standards, community-based social marketing practices promulgated by the MA Department of Environmental Protection and the Division of Ecological Restoration, and other new technological tools.